Parallel Architectures
UFO
WP3: Data processing, evaluation, and visualization
Agenda
  I. Current Status:
Fast Tomographic Reconstruction,
Hardware Platform Review,
Streaming Setup,
IPE Software Stack
  II. Working Plan:
Sub Packages of WP3,
IPE Developments
A flightless weevil
[Speaker Notes: Zu Antrag Prämienbudget]

---
Hardware
Overview: GPU Computing
Highly parallel architecture: up to 480 parallel threads in the current NVIDIA architecture
Up to 16 GPU cores in a single PC
Rich set of libraries (FFT, BLAS, Lapack)
OpenCL is an industry standard.
Mass market: rapid development and cheap prices (cards are below 300 EUR)
AMD Opeteron 6176 (1500$)
Number of cores:	12
Frequency of cores:	2.3 Ghz
Peak performance:	110.4/55.2 GFlop/s
NVIDIA GeForce GTX580 (500$)
Parallel processors:	512
Frequency of cores:	1.5 GHz
Peak performance:	1581 / 197(515) GFlops
ATI Radeon HD 5970 (~700$)
Parallel processors:	2 x 1600
Frequency of cores:	725 MHz
Peak performance:	1640 / 928 GFlops

---
WP 3: Deliverables
3.1 Framework for Parallel Computing
GPU Computing Platform
Defining Interfaces, Naming Conventions, Languages
Parallel Computing Framework with Examples
3.2 Development of Data Processing and Assessment Algorithms for Streamed Data on Parallel Hardware
Tomographic Reconstruction Library
Laminographic Reconstruction Library
Streaming setup + complete software stack
Assessment Algorithms
3.3 Graphical User Interface and Visualization of Datasets
Control GUI
Visualization

---
Sample Data-Set for Tomography
Porose polyethylene grains in a conical plastic holder
Sample Data Set:
  Number of Projections:	2000
  Resolution of Projections:	1776x1707
  Total Size:	24GB
Resulting 3D Image:
  Resolution:	1691x1331x1311
  Total Size:	11GB
Required Operations:
  Data I/O:	35GB
  Filtering:	~ 0.6 TFlop
  Back Projection:	~ 53.0 TFlop
Maximum Performance Estimation:
Opteron 6176 (~ 110Gflops)	~ 10 minutes
HDD I/O (~ 50 MB/s)	~ 15 minutes

---
WP3.2 Tomography: Performance
	Xeon Server	GPU Desktop	GPU Server
Type of / Computation	CPU / Xeon E5472 / 8 core, 3 GHz	GeForce GTX 280 / 1 core	2 x GTX295 + 2 x GTX480 / 6 cores
CPU	2 x Xeon E5472	Core2 E6300	2 x Xeon E5540
Memory	16GB DDR3	4GB DDR2	96GB DDR3
HDD	WDC5000AACS	WDC5000AACS	2 x Intel X25-E / Raid-0
Price	5500$ (2000$ CPU)	1000$ (400$ GPU)	9000$ (2000$ GPU, 800$ SSD)
Software	SuSe 11.2, CUDA 3.0, MKL 10.2.1, gcc4.4 -O3 -march=nocona -mfpmath=sse
time (seconds)

---
WP3.2 Tomography: Scalability
2.5%
Back Projection using Tesla S1070
Gflop/s

---
WP3.2 Tomography: Algorithm
Image Loader
Pool of Sinograms
   (host memory)
Pool of CPU and GPU
processing threads
Pool of Vertical Slices
(host memory)
Texture
Data Storage
W
H
GPU thread
1st Stage
2nd Stage
Double
buffering
Double
buffering
Filtering
PCIe Data
Transfer
PCIe Data
Transfer
Fetch slices
for processing
Store results

---
WP3.1 Platform: GPU Comparison
Ratio of Operations
	Tesla C1060	GTX280	GTX295	GTX480
Architecture	GT200	GT200	GT200	Fermi
Processors	1 x 240 @ 1.25GHz	1 x 240 @ 1.3 GHz	2 x 240 @ 1.3 GHz	1 x 480 @ 1.4 GHz
Memory	4 GB @ 177 GB/s	1 GB @ 142 GB/s	900 MB @ 112 GB/s	1.5 GB @ 177 GB/s
Texture	48 GT/s	48 GT/s	46 GT/s	42 GT/s
Power Cons.	188 W	236 W	289 W	250 W
Price	$500	$250	$400	$500
Scalability

---
WP3.1 Platform: Storage Evaluation
MB/s

---
WP3.1 Platform: Conclusion
SuperMicro 7046GT-TRF (~8000$ = 2 Xeon + 4 GPU + 96 GB)
Chipset: Dual Intel 5520, 72 PCIe 2.0 lanes
Memory: 12 DDR3 slots (192GB max)
PCIe 2.0 x16: 4 (full speed),
PCIe 2.0 x4: 2 (in x16 slots); PCIe 1.0 x4: (in x8 slot)
Max Peak Performance (NVidia): 7.15 TFlops / 2.5 Tflops
SuperMicro 7046GT-TRF (~8000$ = 2 Xeon + 4 GPU + 96 GB)
Chipset: Dual Intel 5520, 72 PCIe 2.0 lanes
Memory: 12 DDR3 slots (192GB max)
PCIe 2.0 x16: 4 (full speed),
PCIe 2.0 x4: 2 (in x16 slots); PCIe 1.0 x4: (in x8 slot)
Max Peak Performance (NVidia): 7.15 TFlops / 2.5 Tflops
FrameGrabber
MicroEnable IV
CameraLink Interface
800 MB/s
4 x
30s per 3D image (3GPix)
92 Megapixels/s
GTX295
4 x
Read: 1420 MB/s
Write: 1060 MB/s
SSD / Raid-0
Intel Pro/10Gbe
10 Gb network
LSDF
Large Scale Data Facility

---
WP3.1 Platform: Scaling
Cyclone PCIe2-2707
External PCIe Box
3 x
3 times more GPUs,
PCIe I/O is not a problem

---
WP 3.2: Streaming Setup

---
WP3.3: Camera Control

---
WP3.1: IPE Toolset
Coding:
Libraries in pure C (at least with C-interfaces)
GLib for a library implementing various primitives
Applications using scripting languages (Ruby, Python, ...)
Glade (GTK) for User Interfaces
Collaborative Tools:
CMake build system
Distributed revision control (Bazaar, GIT, ...)
Trac for project management and bug tracking

---
WP3.1: Software Platform
Compiler flags
Intel: -O3 -xS (with SSE vectorization)
Gcc/LLVM: -O3 -march=nocona (with SSE vectorization)
Decision: Using 'gcc' and 'Intel MKL' in all benchmarks
Filtering
(FFT Library Benchmark)
Back Projection
(Compiler Benchmark)
Gflop/s
Gflop/s

---
WP 3.1 + 3.2: Framework
Level 3
Scheduling / Load Balancing
Level 2
Control
UI
Tomography
Laminography
Noise Reduction
Filter Abstract Interface
Basic Image Processing Algorithms
Streaming
Setup
Level 1
Format Support, Camera Control, Data Movements
Hardware Abstraction (OpenCL, Camera Drivers)
API

---
Framework: Stages
1. Projection Preprocessing
2. Sinogram Generation
3. Reconstruction
4. Slice Postprocessing
5. Gluing

---
Framework: Filters
Reconstruction
Context
Projections
Sinograms
Slices
Projection
Filters
Sinogram
Filters
Reconstruction
Filter
Context
GPU/CPU ?
Complete Source ?
Block Processing ?
Constructor Func.
Destructor Func.
Process Func.
... filter specific ...
3D Image
Filters
Slice
Filters
process(fctx, rctx, first_chunk, number_of_chunks)

---
Framework: Tomography
Projections
Noise
Reduction
Sinogram
Generation
Sinograms
Slices
Fourier
Filter
Back
Projection

---
Framework: Filter Chains
GPU
Memory
GPU
Filter 1
GPU
Filter 1
GPU
Filter 1
GPU
Filter 2
Filter
Needing
Complete
Data Set
Main
Memory
Previous
Stage
CPU
Filter 3
Transfers data between GPU and Main Memory itself
Copy to
GPU
Memory
Back to
System
Memory

---
WP 3.1: Deliverables
GPU Computing Platform
Test connection with LSDF (IPE)
Build new platform when PCIe 3.0 is available (IPE)
Defining Interfaces, Naming Conventions, Languages
Evaluate OpenCL platform (IPE)
Define a set of base libraries and languages for platform (All)
Define a coding style, naming scheme, interfaces (All)
Parallel Computing Framework with Examples
Infrastructure layer to control hardware and transfer data from camera to system memory and GPU (IPE); Integration with Tango/SPEC (TPU, KIT)
Basic Image Processing Algorithms - Noise reduction and other image preprocessing and postprocessing algorithms (TPU)
Load balancing, task scheduling, and other management code (IPE)

---
WP 3.2: Deliverables
Reconstruction Library and Application
Tomography: Migrate PyHST to OpenCL, DePythonize, and adjust to agreed coding standards (IPE)
Laminography: Optimize for GPU architecture (UCA, IPE)
Algebraic Reconstruction (SCI, UCA)
Integrate all developed code and provide application managing complete data flow from camera to 3D image (IPE, UCA)
Assessment Algorithms
Development of assessment algorithms (IPE, UCA)

---
WP 3.3: Deliverables
GUI
Control GUI (TPU)
Visualization (UCA)
Prototype of 3D Visualization
application by UCA

---
Summary for IPE
PyHST as
PyHST is a basis of framework!
Port PyHST to OpenCL and evaluate performance (WP3.1)
Negotiate libraries, languages, and coding standards (WP3.1)
First level of framework: organize flow of data from the camera to PyHST (WP3.1 + WP3.2)
Split PyHST into the FBP algorithm (framework, level 2) and basis of management code scheduling and load balancing code (framework, level 3). Move remaining Python code to C/OpenCL. Modify the code to follow negotiated standards (WP3.1, WP3.2)
Adjust the software stack to fit needs of laminography case (WP3.1)
Integrate mandatory pre/post-filtering code
Provide a first version of the complete application (WP3.2)
Complete integration with TANGO and other ANKA infrastructure (WP3.1)
Assemble second generation of computation platform (WP3.1)
Work on performance improvement, additional algorithms, assessment
4
7
12

---
Additional Slides

---
WP3.1 Platform: GPU Platforms
Asus Rampage III Extreme (1800$ = Core i5 + 2 x GTX295 + 8 GB)
Chipset: x58, 36 PCIe 2.0 lanes; 6 DDR3 slots (48 GB max)
PCIe 2.0 x16: 4 (x8 if all 4 are used)
Max Peak Performance (ATI): 18.56 Tflops / 3.7 Tflops
Max Peak Performance (NVidia): 7.15 Tflops / 595 GFlops
Asus + 2 x GTX295
  966 GF/s
1800 $
Desktop + GTX280
232 GF/s
800 $
Standard Desktop (800$ = Core2 + GTX285 + 2 GB)
SuperMicro 7046GT-TRF (~8000$ = 2 Xeon + 4 GPU + 96 GB)
Chipset: Dual Intel 5520, 72 PCIe 2.0 lanes, 12 DDR3 slots (192GB max)
PCIe 2.0 x16: 4 (full speed), x4: 2 (in x16 slots); PCIe 1.0 x4: (in x8 slot)
Max Peak Performance (ATI): 18.56 TFlops / 3.7 Tflops
Max Peak Performance (NVidia): 7.15 TFlops / 2.5 Tflops
SuperMicro + 4 GPU
1503 GF/s
8000 $
NVIDIA Tesla S1070
NVIDIA Tesla S1070 (~8000$ + 4000$ host)
System: Requires separate host server
GPU Devices: 4 x Tesla C1060 (960 parallel processors at 1.44 GHz)
Peak performance:	4.14 Tflops / 345 Gflops
GPU Memory Size: 16 GB
    873 GF/s
12000 $
2 Intel Xeon 5472
    50 GF/s
5500 $
Dual Xeon 5472 Server (5500$ = 16 GB)
Max Peak Performance: 96 Gflops / 48 GFlops
Coolfax CXT8000
Coolfax CXT8000 (36000$ = 2 Xeon + 8 Tesla C2050 + 144GB)
Chipset: Dual Intel 5520, 72 PCIe 2.0 lanes
PCIe Switch: PLX PEX8647; PCIe 2.0 x16: 8 (full speed)
18 DDR3 Memory Slots: 288 GB max
Max Peak Performance: 10 Tflops / 5 Tflops
Back Projection Performance: 2336 Gflops (Estimated)