## Slide 1
Status report: Design of UFO experimental station

## Slide 2: Functional components
Table
Sample manipulator
  Tomography / Laminography
  High-speed tomography
  Rocking Curve Imaging
Detector manipulator
  Main detector
  RCI detector
Sample changer
Sample environment

## Slide 3: Table
Base to mount all manipulators
Movable in beam line via air pads
Required degrees of freedom: height, pitch, yaw
  Height: compensate offset between white and monochromatic beam
  Pitch, yaw: align detector translation parallel to beam

## Slide 4: Sample manipulator
Provide necessary degrees of freedom to perform scans
Modular design to cover broad demands for different imaging modalities

## Slide 5: Sample manipulator: Tomography/Laminography
Point to point motion and slow continuous tomography
Degrees of freedom below axis of rotation
  Rotation, unlimited travel, large central aperture, 120 RPM
  Translation vertical, > 50 mm (select sample height, spiral CT)
  Translation horizontal, > 100 mm (flat fields, sample)
  Pitch, < +- deg (align axis of rotation w. r. t. detector pixels)
  Roll, < +- 5 deg (align axis of rotation w. r. t. detector pixels)
  Large Roll, > 60 deg (switch between tomography and laminography, RCI scan)
Degrees of freedom above axis of rotation
  Translation parallel to beam > 100 mm (select region for tomography / laminography)
  Translation perpendicular to the beam > 100 mm (select region for tomography / laminography)
Serves as basis to mount module for additional imaging modalities

## Slide 6: Module: High- speed tomography
Moderate to high- speed tomography
Degrees of freedom:
  High-speed rotation (6000 RPM)
  Vertical translation, constant speed range > 50 mm (select sample height, spiral CT)

## Slide 7: Module: Rocking Curve Imaging
Scan samples with high precision in 6 degrees of freedom
  Hexapod mounted in central aperture
ToDo: specify required travel ranges and precision

## Slide 8: Detector manipulator
Provide necessary degrees of freedom to position main detector system
Main detector manipulator
  Long translation parallel to beam, > 1000 mm (select sample-detector distance)
  Vertical translation, > 100 mm (compensate for small beam height offsets)
  Horizontal translation, > 100 mm (compensate switch from split to not split mode)
RCI detector manipulator
  Position detector for RCI scans
  Degrees of freedom:
    Vertical circle around sample
    Distance

## Slide 9: Module: Sample Changer
Enable high throughput and sample batches
Degrees of freedom:
  Vertical translation
  Horizontal translation, perpendicular and parallel to beam
Needs to be compatible with tomography and laminography samples of reasonable size (< 30 mm diameter)
Sample changer design requires detailed design of detector and sample manipulator mechanics
Status
  Early specification phase

## Slide 10: Module: Sample environment
Change environmental conditions of sample during scan
Compatible with tomographic and laminographic geometry
Starting point: mirror furnace from Universtiy of Freiburg

## Slide 11: Status
Discussions with companies started
  Aerotech for sample and detector manipulator
  Elya for detector system
Next steps
  Discussion with University of Freiburg concerning sample environment
  Further refinement of specifications, especially RCI manipulators
  Update concept drawings
  Evaluate possibility to construct setup in-house (especially detector mechanics)
  Finalize design
Deadline
  Setup delivery Summer 2012